# Text boxes

July/2013

Introduction of the ICH climate chamber and the ICP cooled incubator of Memmert Generation 2012

Memmert introduces two more Generation 2012 appliances in August 2013. Especially the optimisation of the user friendliness, network compatibility, documentation and programming were focused on.

Both appliances have an intuitively operable touch screen, the so-called ControlCOCKPIT, intelligently designed door handles that guarantee vibration-free opening and closing of the door, even with the elbows or feet, and recessed grips for safe transport to and from the laboratory.

Intuitive operation with “Touch, turn & go”

Both constant climate chambers ICH and cooled incubators ICP feature a ControlCOCKPIT TwinDISPLAY, which uses both operating fields for settings and display due to the wide range of functions. The convenient functions are supplemented with modern communication interfaces and the logging and documentation software AtmoCONTROL.

(BU) Memmert cooled incubator ICP 750

…

The ICH climate chamber – Unique homogeneity for long-term ambient conditions

The ICH air jacket temperature control system brings both hot and cold into the interior in a uniform manner. The resulting high homogeneity of temperature and humidity fulfils the most important requirements to a stability test chamber. For stability tests in accordance with ICH Q1A, it covers a temperature range from -10 °C to +60°C and a relative humidity range from 10 to 80 %.

With the help of the illumination unit in the ICH L model, photo stability tests can be performed in accordance with standard ICH Q1B, option 2. Thanks to a combination of the parameters temperature, humidity and CO2, the climate chamber ICH C model can also be universally applied for building material tests or for applications in the field of cell biology that require temperatures below room temperature.

As a supplement to the appliance with 256 litres of chamber volume that is available so far, Memmert is also including climate chambers with a 108-litre as well as 749-litre chamber volume in its new Generation 2012 programme.

The ICP cooled incubator – Fast heating up and cooling down in ramp operation

In life sciences, modern food analytics and in cosmetic research, tests and processes must be reproducible and documentable under precisely defined conditions. Therefore, the ICP cooled incubator is available with a TwinDISPLAY in the comfort version as a standard. Due to the finely adjusted control technology, temperatures reach the set point precisely, without any energy-intensive surge heating, and thus no temperature overshoots that could be a hazard for the chamber load. The air jacket temperature control system guarantees the user of the ICP high temperature homogeneity without icing of the cooling unit and prevents dehumidification of the interior or drying out of the samples. The ICP model series operates in a temperature range of -12 to +60 °C (ICP 55 from -5 °C) and has a chamber volume between 53 and 749 litres.

Responsible for content:

Memmert GmbH & Co. KG

Katja Rosenke

PO Box 1720

D-91107 Schwabach

Telephone: (0) 9122/925-177

Fax: (0) 9122/14585

Email: presse@memmert.com

E-Mail: presse@memmert.com